## Slide 1: The Nanokernel
David L. Mills
University of Delaware
http://www.eecis.udel.edu/~mills
mailto:mills@udel.edu

## Slide 2: Going faster and faster
Observing that
  PC and workstation processor clock rates approaching and exceeding 1 GHz are becoming widely deployed
  10-Mb Ethernets have been replaced by 100-MHz Ethernets and these are now being replaced by 1-GHz Ethernets
  1.5-Mb Internet links have been replaced by 43-Mb links and these are being replaced by 155-Mb OC-3 links and soon 2.4-Gb OC-48 links
And further that
  Timekeeping expectations have been typically tens of milliseconds on a WAN and low milliseconds on a LAN
  Timekeeping ambitions for some applications are in the tens of microseconds on a modern workstation
We conclude that
  Accuracy expectations can be considerably improved by moving the clock discipline code from user space to the kernel and, where available, precision synchronization sources

## Slide 3: Evolution to NTP Version 4
NTP Version 3 was first used in 1992 in a rambunctious Internet of congested links and 25-MHz workstations
NTP Version 4 architecture, protocol and algorithms have been evolved for gigabit networks and gigahertz computers
  Improved clock models which accurately predict the phase and frequency noise for each synchronization source and network path
  Engineered algorithms which reduce the impact of delay spikes and oscillator wander while speeding up initial convergence
  Redesigned clock discipline algorithm which can operate in frequency-lock, phase-lock and hybrid modes
But, the Unix time adjustment primitive prevents further improvement to the ambition of a few microseconds

## Slide 4: Unix time adjustment primitive
A
B
C
t
Frequency Error
+S

Adjustment RateR
The discipline needs to steer the frequency over the range ±S, but the intrinsic clock frequency error is 
Unix adjtime() slews frequency at rate R   PPM beginning at A
Slew continues to B, depending on the programmed frequency steer
Offset continues to C with frequency offset due to error 
The net error with zero steering is which can be several hundred s
Adjustment Interval

S

## Slide 5: Computer clock modelling
Pentium 200
SPARC IPC
Resolution limit
Alpha 433

## Slide 6: Allan intercepts compared
System | Resolution | Precision | Stability | x Intercept | y Intercept | Range *
SPARC IPC | 1000 ns | 1000 ns | good | 2000 s | .01 PPM | 600 - 5000 s
Pentium 200 | 1 ns | 5 ns | poor | 50 s | .03 PPM | 10 - 300 s
Alpha 433 | 1 ns | 2.3 ns | good | 200 s | .005 PPM | 50 - 2000 s
Resolution limit | 1 ns | 1 ns | good | 2 s | .0004 PPM | 1 - 10 s
* For stability no worse than twice y intercept

## Slide 7: NTP kernel clock discipline
Type II, adaptive-parameter, hybrid phase/frequency-lock loop disciplines variable frequency oscillator (VFO) phase and frequency
NTP daemon computes phase error Vd = r o between source and VFO, then grooms samples to produce time update Vs
Loop filter computes phase x and frequency y corrections and provides new adjustments Vc at 1-s intervals
VFO frequency is adjusted at each hardware tick interrupt
Vd
Vc
Phase/Freq Prediction
Clock
Filter
Clock Adjust
Phase
Detector
VFO
Vs
r+
c
NTP
Loop Filter
x
y
NTP
Daemon
Kernel

## Slide 8: FLL/PLL prediction functions
yPLL
PLL Predict

Vs
x
Phase Correct
y
yFLL
FLL Predict
Vs is the phase offset produced by the clock filter algorithm
x is the phase correction computed as a fraction of Vs
yFLL is the frequency adjustment computed as the average of past frequency offsets
yPLL is the frequency adjustment computed as the integral of past phase offsets
yFLL and yPLL are combined according to weight factors determined by poll interval and Allan deviation characteristic

## Slide 9: Nanokernel architecture
PLL/FLL discipline predicts phase x and frequency y at measurement intervals from 1 s to over one day
PPS discipline predicts phase and frequency at averaging intervals from 4 s to 256 s, depending on nominal Allan intercept
On overflow of the clock second, a new value is calculated for the tick interrupt adjustment
Tick adjustment is added to the system clock at every tick interrupt
Process cycle counter (PCC) used to interpolate microseconds or nanoseconds between tick interrupts
PLL/FLL
Discipline
Clock Oscillator
PPS Discipline
PPS
Interrupt
Tick Interrupt
NTP
Update
Second Overflow
Frequency
Prediction
Phase
Prediction
Calculate Adjustment
x
y

## Slide 10: PPS phase and frequency discipline
Phase and frequency disciplined separately - phase from system clock offset relative to second, frequency from process cycle counter (PCC)
Frequency discriminator rejects noise and incorrect frequency sources
Median filter rejects sample outlyers and provides error statistic
Range checks reject popcorn spikes in phase and frequency
Phase offsets exponentially averaged with variable time constant
Frequency offsets averaged over variable interval
Phase
Average
Frequency Discrim
Frequency
Average
y
PPS Interrupt
x
Range
Checks
Range Checks
Median Filter
Ambiguity Resolve
Second Offset
PCC Counter

## Slide 11: Experimental results with PPS discipline
Hepzibah is a 400-MHz Pentium workstation with a GPS receiver
  The PPS signal is connected via parallel port and modified driver
Rackety is a 25-MHz SPARC IPC dedicated NTP server with dual redundant GPS receivers and dual redundant WWVB receivers
  This machine has over 1000 clients causing a load of 15 packets/sec
  The PPS signal is connected via serial port and modified driver
Churchy is a 433-MHz Alpha workstation with a GPS receiver
  This machine uses a SAW oscillator presumed spectrally pure
  The PPS signal is connected via serial port and modified driver
All machines accessed the PPS signal from a GPS receiver and a level converter where necessary
Experiments lasted one day with data collected by the NTP daemon

## Slide 12: PPS time offset characteristic for Hepzibah
Jitter is presumed caused by interrupt latencies on the ISA bus
We need to explain why the spikes are both positive and negative

## Slide 13: PPS time offset characteristic for Rackety
Jitter is presumed caused by interrupt latencies on the Sbus
Large negative spikes reflect contention by the radios and network

## Slide 14: PPS time offset characteristic for Churchy
Jitter is presumed caused by interrupt latencies on the PCI bus
High flicker noise may be due to SAW phase noise and no PLL

## Slide 15: Present status
The kernel modifications have been implemented for FreeBSD, Linux, Alpha and SunOS
The current version is in current FreeBSD and Linux public distributions
An older version, but with resolution only to the microsecond, is in current Alpha and Solaris licensed products
A standard PPS application program interface (PPSAPI) has been proposed to the IETF and supported in all kernels

## Slide 16: Further information
Network Time Protocol (NTP): http://www.ntp.org/
  Current NTP Version 3 and 4 software and documentation
  FAQ and links to other sources and interesting places
David L. Mills: http://www.eecis.udel.edu/~mills
  Papers, reports and memoranda in PostScript and PDF formats
  Briefings in HTML, PostScript, PowerPoint and PDF formats
  Collaboration resources hardware, software and documentation
  Songs, photo galleries and after-dinner speech scripts
FTP server ftp.udel.edu (pub/ntp directory)
  Current NTP Version 3 and 4 software and documentation repository
  Collaboration resources repository
Related project descriptions and briefings
  See “Current Research Project Descriptions and Briefings” at http://www.eecis.udel.edu/~mills/status.htm