## Slide 1: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 2: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
Pipelined and time-varying window size:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 3: TCP Header
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
Internet
checksum
(as in UDP)
flow control
reliability
multiplexing
20 bytes header. It is quite big.

## Slide 4: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  reliable data transfer
    sequence numbers
    RTO
    fast retransmit
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 5: TCP reliable data transfer
TCP creates transport service on top of IP’s unreliable service
Approach (similar to Go-Back-N/Selective Repeat)
  Send a window of segments
  If a loss is detected, then resend
Issues
  Sequence numbering – to identify which segments have been sent and are being ACKed
  Detecting losses
  Which segments are resent?
Note: we will only consider TCP-Reno. There are several other versions of TCP that are slightly different.

## Slide 6: TCP reliable data transfer
TCP creates transport service on top of IP’s unreliable service
Approach (similar to Go-Back-N/Selective Repeat)
  Send a window of segments
  If a loss is detected, then resend
Issues
  Sequence numbering – to identify which segments have been sent and are being ACKed
  Detecting losses
  Which segments are resent?
Note: we will only consider TCP-Reno. There are several other versions of TCP that are slightly different.

## Slide 7: TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
  It can be used as a pointer for placing the received data in the receiver buffer
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 8: TCP sequence numbers and ACKs
110
108
H
E
L
L
O
W
O
R
L
D
101
102
103
104
105
106
107
109
111
Byte numbers
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Seq no: 12
ACK no:
Data:
Length: 0
Seq no: 104
ACK no: 12
Data: LO W
Length: 4
Seq no: 12
ACK no:
Data:
Length: 0
104
108
Seq. #’s:
  byte stream “number” of first byte in segment’s data
  It can be used as a pointer for placing the received data in the receiver buffer
ACKs:
  seq # of next byte expected from other side
  cumulative ACK

## Slide 9: TCP sequence numbers and ACKs- bidirectional
110
108
H
E
L
L
O
W
O
R
L
D
101
102
103
104
105
106
107
109
111
Byte numbers
G
O
O
D
B
U
Y
12
13
14
15
16
17
18
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Seq no:
ACK no:
Data: GOOD
Length: 4
Seq no:
ACK no:
Data: LO W
Length: 4
Seq no:
ACK no:
Data: BU
Length: 2
12
104
104
16
108
16

## Slide 10: TCP reliable data transfer
TCP creates transport service on top of IP’s unreliable service
Approach (similar to Go-Back-N/Selective Repeat)
  Send a window of segments
  If a loss is detected, then resend
Issues
  Sequence numbering – to identify which segments have been sent and are being ACKed
  Detecting losses
    Timeout
    Duplicate ACKs
  Which segments are resent?
Note: we will only consider TCP-Reno. There are several other versions of TCP that are slightly different.

## Slide 11: Timeout
RTO
If an ACK is not received before RTO (retransmission timeout), a timeout is declared
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Timeout event:
Retransmit segment
Seq no: 12
ACK no:
Data:
Length: 0

## Slide 12: Timeout
RTO
If an ACK is not received before RTO (retransmission timeout), a timeout is declared
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Timeout event:
Retransmit segment
RTO is too long.
Waste time = waste bandwidth
Seq no: 12
ACK no:
Data:
Length: 0

## Slide 13: Timeout
RTO
If an ACK is not received before RTO (retransmission timeout), a timeout is declared
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Spurious timeout event:
Retransmit segment
Seq no: 12
ACK no:
Data:
Length: 0
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
RTO is too small.
Retransmission was not needed
== wasted bandwidth

## Slide 14: Timeout
RTO
If an ACK is not received before RTO (retransmission timeout), a timeout is declared
Seq no: 101
ACK no: 12
Data: HEL
Length: 3
Timeout event:
Retransmit segment
Seq no: 12
ACK no:
Data:
Length: 0
RTO is just right; a timeout would occur just after the ACK should arrive
RTO = RTT+ a little bit

## Slide 15: RTT
The network must have buffers (to enable statistical multiplexing)
The buffer occupancy is time-varying
  As flows start and stop, congestion grows and decreases, causing buffer occupancy to increase and decrease.
RTT is time-varying. There is no single RTT.
Solution: make RTO a function of a smoothed RTT
buffers

## Slide 16: Smooth RTT
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125

## Slide 17: TCP Round Trip Time and Timeout
Setting the timeout (RTO)
RTO = EstimtedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
first estimate of how much SampleRTT deviates from EstimatedRTT:
RTO = EstimatedRTT + 4*DevRTT
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
Then set timeout interval:

## Slide 18: TCP Round Trip Time and Timeout
RTO = EstimatedRTT + 4*DevRTT
Might not always work
RTO = max(MinRTO, EstimatedRTT + 4*DevRTT)
MinRTO = 250 ms for Linux
500 ms for windows
1 sec for BSD
So in most cases RTO = minRTO
Actually, when RTO>MinRTO, the performance is quite bad; there are many spurious timeouts.
Note that RTO was computed in an ad hoc way. It is really a signal processing and queuing theory question…

## Slide 19: RTO details
When a pkt is sent, the timer is started, unless it is already running.
When a new ACK is received, the timer is restarted
Thus, the timer is for the oldest unACKed pkt
  Q: if RTO=RTT+, are there many spurious timeouts?
  A: Not necessarily
RTO
ACK arrives, and so RTO timer is restarted
RTO
RTO
RTO
This shifting of the RTO means that even if RTO<RTT, there might not be a timeout.
However, for the first packet sent, the timer is started. If RTO<RTT of this first packet, then there will be a spurious timeout.
While it is implementation dependent, some implementations estimate RTT only once per RTT.
The RTT of every pkt is not measured.
Instead, if no RTT is being measured, then the RTT of the next pkt is measured. But the RTT of retransmitted pkts is not measured
Some versions of TCP measure RTT more often.

## Slide 20: TCP reliable data transfer
TCP creates transport service on top of IP’s unreliable service
Approach (similar to Go-Back-N/Selective Repeat)
  Send a window of segments
  If a loss is detected, then resend
Issues
  Sequence numbering – to identify which segments have been sent and are being ACKed
  Detecting losses
    Timeout
    Duplicate ACKs
  Which segments are resent?
Note: we will only consider TCP-Reno. There are several other versions of TCP that are slightly different.

## Slide 21: Lost Detection
sender
receiver
Send pkt0
Send pkt2
Send pkt3
Send pkt4
Send pkt5
Send pkt6
Send pkt7
Send pkt8
Send pkt9
Send pkt10
Send pkt11
TO
Send pkt12
Send pkt13
Send pkt6
Send pkt7
Send pkt8
Send pkt9
Rec 0, give to app, and Send ACK no= 1
Rec 1, give to app, and Send ACK no= 2
Rec 2, give to app, and Send ACK no = 3
Rec 3, give to app, and Send ACK no =4
Rec 4, give to app, and Send ACK no = 5
Rec 5, give to app, and Send ACK no = 6
Rec 7, save in buffer, and Send ACK no = 6
Rec 8, save in buffer, and Send ACK no = 6
Rec 9, save in buffer, and Send ACK no = 6
Rec 10, save in buffer, and Send ACK no = 6
Rec 11, save in buffer, and Send ACK no = 6
Rec 12, save in buffer, and Send ACK no= 6
Rec 13, save in buffer, and Send ACK no=6
Rec 6, give to app,. and Send ACK no =14
Rec 7, give to app,. and Send ACK no =14
Rec 8, give to app,. and Send ACK no =14
Rec 9, give to app,. and Send ACK no=14
It took a long time to detect the loss with RTO
But by examining the ACK no, it is possible to determine that pkt 6 was lost
Specifically, receiving two ACKs with ACK no=6 indicates that segment 6 was lost
A more conservative approach is to wait for 4 of the same ACK no (triple-duplicate ACKs), to decide that a packet was lost
This is called fast retransmit
Triple dup-ACK is like a NACK

## Slide 22: Fast Retransmit
Send pkt14
sender
receiver
Send pkt0
Send pkt2
Send pkt3
Send pkt4
Send pkt5
Send pkt6
Send pkt7
Send pkt8
Send pkt9
Send pkt10
Send pkt11
Send pkt6
Send pkt12
Send pkt13
Send pkt15
Send pkt16
Rec 0, give to app, and Send ACK no= 1
Rec 1, give to app, and Send ACK no= 2
Rec 2, give to app, and Send ACK no = 3
Rec 3, give to app, and Send ACK no =4
Rec 4, give to app, and Send ACK no = 5
Rec 5, give to app, and Send ACK no = 6
Rec 7, save in buffer, and Send ACK no = 6
Rec 8, save in buffer, and Send ACK no = 6
Rec 9, save in buffer, and Send ACK no = 6
Rec 10, save in buffer, and Send ACK no = 6
Rec 11, save in buffer, and Send ACK no = 6
Rec 6, save in buffer, and Send ACK= 12
Rec 12, save in buffer, and Send ACK=13
Rec 13, give to app,. and Send ACK=14
Rec 14, give to app,. and Send ACK=15
Rec 15, give to app,. and Send ACK=16
Rec 16, give to app,. and Send ACK=17
first dup-ACK
second dup-ACK
third dup-ACK
Retransmit pkt 6

## Slide 23: Which segments to resend?
Recall, in go-back-N, all segments in the window are resent. However, in TCP …
Cumulative ACK only (TCP-Reno+TCP-New Reno): retransmit the missing segment, and assume that all other unACKed segments were correctly received.
Selective ACK (TCP-SACK): retransmit any missing segment (or holes in the ACKed sequence numbers)

## Slide 24: Delayed ACKs
ACKs use bandwidth.
What happens if an ACK is lost?
  Not much, cumulative ACKs mitigate the impact of lost ACKS
  (of course, if too many ACKs are lost, then timeout occurs)
To reduce bandwidth, only send fewer ACKS
Send one ACK for every two segments

## Slide 25: TCP ACK generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms (200ms)
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 26: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 27: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
Internet
checksum
(as in UDP)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)

## Slide 28: TCP Flow Control
receive side of TCP connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
The sender never has more than a receiver windows worth of bytes unACKed
This way, the receiver buffer will never overflow
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 29: Flow control – so the receive doesn’t get overwhelmed.
The number of unacknowledged packets must be less than the receiver window.
As the receivers buffer fills, decreases the receiver window.
Seq#=20
Ack#=1001
Data = ‘Hi’, size = 2 (bytes)
Seq#=1001
Ack#=24
Data size =0
Rwin=0
Seq#=22
Ack#=1001
Data = ‘By’, size = 2 (bytes)
Seq#=4
Ack#=1001
Data = ‘e’, size = 1 (bytes)
Seq#=1001
Ack#=22
Data size =0
Rwin=2
Seq#=1001
Ack#=24
Data size =0
Rwin=9
15
buffer
Seq #
SYN had seq#=14
16
17
18
19
20
21
22
S
t
e
v
e
H
i
S
t
e
v
e
H
i
B
y
15
16
17
18
19
20
21
22
24
25
26
27
28
29
30
31
Application reads buffer
24
25
26
27
28
29
30
31
e
The rBuffer is full

## Slide 30
Seq#=20
Ack#=1001
Data = ‘Hi’, size = 2 (bytes)
Seq#=1001
Ack#=24
Data size =0
Rwin=0
Seq#=22
Ack#=1001
Data = ‘By’, size = 2 (bytes)
Seq#=1001
Ack#=22
Data size =0
Rwin=2
buffer
Seq#=1001
Ack#=24
Data size =0
Rwin=9
Seq#=1001
Ack#=24
Data size =0
Rwin=9
3 s
Seq#=4
Ack#=1001
Data = ‘e’, size = 1 (bytes)
15
Seq #
SYN had seq#=14
16
17
18
19
20
21
22
S
t
e
v
e
H
i
S
t
e
v
e
H
i
B
y
15
16
17
18
19
20
21
22
24
25
26
27
28
29
30
31
Application reads buffer
24
25
26
27
28
29
30
31
e
Seq#=24
Ack#=1001
Data = , size = 0 (bytes)
window probe

## Slide 31
Seq#=20
Ack#=1001
Data = ‘Hi’, size = 2 (bytes)
Seq#=1001
Ack#=24
Data size =0
Rwin=0
Seq#=22
Ack#=1001
Data = ‘By’, size = 2 (bytes)
Seq#=1001
Ack#=22
Data size =0
Rwin=2
15
buffer
Seq #
SYN had seq#=14
16
17
18
19
20
21
22
S
t
e
v
e
H
i
S
t
e
v
e
H
i
B
y
15
16
17
18
19
20
21
22
Seq#=4
Ack#=1001
Data = , size = 0 (bytes)
3 s
Seq#=1001
Ack#=24
Data size =0
Rwin=0
6 s
Seq#=4
Ack#=1001
Data = , size = 0 (bytes)
Max time between probes is 60 or 64 seconds
The buffer is still full

## Slide 32: Receiver window
The receiver window field is 16 bits.
Default receiver window
  By default, the receiver window is in units of bytes.
  Hence 64KB is max receiver size for any (default) implementation.
  Is that enough?
    Recall that the optimal window size is the bandwidth delay product.
    Suppose the bit-rate is 100Mbps = 12.5MBps
    2^16 / 12.5M = 0.005 = 5msec
    If RTT is greater than 5 msec, then the receiver window will force the window to be less than optimal
    Windows 2K had a default window size of 12KB
Receiver window scale
  During SYN, one option is Receiver window scale.
  This option provides the amount to shift the Receiver window.
  Eg. Is rec win scale = 4 and rec win=10, then real receiver window is 10<<4 = 160 bytes.
64KB sent
5msec
RTT
Notes: Q: In the figure above, give the formula for the maximum data rate as a function of receiver window and RTT.

## Slide 33: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 34: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
  Establish options and versions of TCP
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies initial seq #
  no data
Step 2: server host receives SYN, replies with SYNACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data

## Slide 35: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
Internet
checksum
(as in UDP)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)

## Slide 36: Connection establishment
Seq no=2197
Ack no = xxxx
SYN=1
ACK=0
Send SYN
Reset the sequence number
The ACK no is invalid
Seq no = 12
ACK no = 2198
SYN=1
ACK=1
Send SYN-ACK
Although no new data has arrived, the ACK no is incremented (2197 + 1)
Seq no = 2198
ACK no = 13
SYN = 0
ACK =1
Send ACK
(for syn)
Although no new data has arrived, the ACK no is incremented (2197 + 1)

## Slide 37: Connection with losses
SYN
3 sec
SYN
2x3=6 sec
SYN
12 sec
SYN
64 sec
Give up
Total waiting time
3+6+12+24+48+64 = 157sec

## Slide 38: SYN Attack
attacker
SYN: to port 80, from port 12344
Reserve memory for TCP connection.
Must reserve enough for the receiver buffer.
And that must be large enough to support high data rate
ignored
SYN-ACK
SYN: to port 80 from 1235
SYN
SYN
SYN
SYN
SYN
SYN
157sec
Victim gives up on first SYN-ACK and frees first chunk of memory

## Slide 39: SYN Attack
attacker
SYN
ignored
SYN-ACK
SYN
SYN
SYN
SYN
SYN
SYN
SYN
157sec
Total memory usage:
  Memory per connection x number of SYNs sent in 157 sec
Number of syns sent in 157 sec:
  157 x 10Mbps / (SYN size x 8) = 157 x 31250 = 5M
Suppose Memory per connection = 20K
Total memory = 20K x 5M = 100GB … machine will crash

## Slide 40: Defense from SYN Attack
If too many SYNs come from the same host, ignore them
attacker
SYN
ignored
SYN-ACK
SYN
SYN
SYN
SYN
SYN
SYN
SYN
ignore
ignore
ignore
ignore
ignore
Better attack
Change the source address of the SYN to some random address

## Slide 41: SYN Cookie
Do not allocate memory when the SYN arrives, but when the ACK for the SYN-ACK arrives
The attacker could send fake ACKs
But the ACK must contain the correct ACK number
Thus, the SYN-ACK must contain a sequence number that is
  not predictable
  and does not require saving any information.
This is what the SYN cookie method does
Seq no=2197
Ack no = xxxx
SYN=1
ACK=0
Send SYN
Reset the sequence number
The ACK no is invalid
Seq no = 12
ACK no = 2198
SYN=1
ACK=1
Send SYN-ACK
Although no new data has arrived, the ACK no is incremented (2197 + 1)
Seq no = 2198
ACK no = 13
SYN = 0
ACK =1
Send ACK
(for syn)
Although no new data has arrived, the ACK no is incremented (2197 + 1)
Allocate
memory

## Slide 42: TCP Connection Management (cont.)
Closing a connection:
Step 1: client end system sends TCP packet with FIN=1 to the server
Step 2: server receives FIN, replies with ACK with ACK no incremented Closes connection,
The server close its side of the conenction whenever it wants (by send a pkt with FIN=1)
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 43: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 44: TCP Connection Management (cont)
TCP client
lifecycle
TCP server
lifecycle

## Slide 45: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 46: Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
On the other hand, the host should send as fast as possible (to speed up the file transfer)
a top-10 problem!
  Low quality solution in wired networks
  Big problems in wireless (especially cellular)

## Slide 47: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
no retransmission
large delays when congested
maximum achievable throughput
unlimited shared output link buffers
Host A
lin : original data
Host B
lout

## Slide 48: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of lost packet
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in : original data, plus retransmitted data

## Slide 49: Causes/costs of congestion: scenario 3
four senders
2-hop paths
Q: what happens as in increases?
The total data rate is the sending rate + the retransmission rate.
finite shared output link buffers
Host A
lin : original data
Host B
lout
’: retransmitted data
A
B
C
D
Host C

## Slide 50: Causes/costs of congestion: scenario 3
Another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
Host A
Host B
lout
Static/Flow Analysis
Definition: p is the prob of pkt loss
Definition: q is the prob of not dropped
Arrival rate at a router:
Fraction of pkts dropped:
1-q = ( + q  - C)/( + q )
( + q ) - q( + q ) =  + q  - C
+ q  - q - q2 =  + q  - C
- q2 =  + q  - C
q2 = q  - C
0=q2 + q  - C
Arrival rate =
 + q 
( + q  - C)/( + q )
Fraction of pkts that make it through =
q2
q2

## Slide 51: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at (XCP)
Two broad approaches towards congestion control:

## Slide 52: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 53: TCP congestion control: additive increase, multiplicative decrease (AIMD)
time
cwnd
Saw tooth
behavior: probing
for bandwidth
In go-back-N, the maximum number of unACKed pkts was N
In TCP, cwnd is the maximum number of unACKed bytes
TCP varies the value of cwnd
Approach: increase transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
    MSS = maximum segment size and may be negotiated during connection establishment. Otherwise, it is set to 576B
  multiplicative decrease: cut cwnd in half after loss not detected by timeout
  Restart cwnd=1 after a timeout

## Slide 54: Additive Increase
When an ACK arrives: cwnd = cwnd + MSS / floor(cwnd/MSS)
cwnd
4000
SN: 1000
AN: 30
Length: 1000
SN: 2000
AN: 30
Length: 1000
inflight
0
ssthresh
0
4000
1000
0
4000
2000
0
SN: 3000
AN: 30
Length: 1000
4000
3000
0
SN: 4000
AN: 30
Length: 1000
4000
4000
0
SN: 30
AN: 2000
RWin: 10000
4250
3000
0
SN: 5000
AN: 30
Length: 1000
4250
4000
0
SN: 30
AN: 3000
RWin: 9000
SN: 6000
AN: 30
Length: 1000
4500
3000
0
4500
4000
0
SN: 30
AN: 4000
Rwin: 8000
SN: 7000
AN: 30
Length: 1000/
4750
3000
0
4750
4000
0
SN: 30
AN: 2000
RWin: 7000
SN: 8000
AN: 30
Length: 1000/
5000
3000
0
5000
4000
0
5000
5000
0
SN: 9000
AN: 30
Length: 1000/
cwndsegment = cwndsegment + 1 / floor(cwndsegment)

## Slide 55: Approximation of AIMD During Pkt Loss
When an ACK arrives: cwndsegment = cwndsegment + 1 / floor(cwndsegment)
When a drop is detected via triple-dup ACK, cwnd = cwnd/2
cwnd
8000
inflight
0
ssthresh
0
8000
1000
0
8000
8000
0
SN: 1MSS. L=1MSS
AN=2000
SN: 2MSS. L=1MSS
SN: 3MSS. L=1MSS
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
SN: 8MSS. L=1MSS
AN=3000
AN=4000
AN=5000
AN=5000
AN=5000
SN: 9MSS. L=1MSS
SN: 10MSS. L=1MSS
SN: 11MSS. L=1MSS
3rd dup-ACK
8125
8000
0
8250
8000
0
8375
8000
0
4000
8000
0
AN=5000
AN=5000
AN=5000
4000
8000
0
4000
8000
0
4000
8000
0
SN: 5MSS. L=1MSS
AN=13MSS
4000
0
0
SN: 14MSS. L=1MSS
SN: 15MSS. L=1MSS
Slow recovery: one RTT is just to retransmit one segment.
Go-Back-N recovers as fast.
We can guess that the dup-acks imply that a segment has been successfully delivered.
AN=5000
SN: 12MSS. L=1MSS
AN=5000
8500
8000
0

## Slide 56: Fast recovery: details
Upon the two DUP ACK arrival, do nothing. Don’t send any packets (InFlight is the same).
Upon the third Dup ACK,
  set SSThres=cwnd/2.
  Cwnd=cwnd/2+3
  Retransmit the requested packet.
Upon every DUP ACK, cwnd=cwnd+1.
If InFlight<cwnd, send a packet and increment InFlight.
When a new ACK arrives, set cwnd=ssthres (RENO).
When an ACK arrives that ACKs all packets that were outstanding when the first drop was detected, cwnd=ssthres (NEWRENO)

## Slide 57: AIMD During Pkt Loss
When an ACK arrives: cwndsegment = cwndsegment + 1 / floor(cwndsegment)
When a drop is detected via triple-dup ACK, cwnd = cwnd/2
cwnd
8000
inflight
0
ssthresh
0
8000
1000
0
8000
8000
0
SN: 1MSS. L=1MSS
AN=2000
SN: 2MSS. L=1MSS
SN: 3MSS. L=1MSS
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
SN: 8MSS. L=1MSS
AN=3000
AN=4000
AN=5000
AN=5000
AN=5000
SN: 9MSS. L=1MSS
SN: 10MSS. L=1MSS
SN: 11MSS. L=1MSS
3rd dup-ACK
8125
8000
0
8250
8000
0
8375
8000
0
7000
8000
4000
AN=5000
AN=5000
AN=5000
8000
8000
4000
9000
9000
4000
10000
10000
4000
SN: 5MSS. L=1MSS
AN=13MSS
4000
3000
0
SN: 16MSS. L=1MSS
AN=5000
SN: 12MSS. L=1MSS
AN=5000
8500
8000
0
SN: 13MSS. L=1MSS
SN: 14MSS. L=1MSS
Upon the third Dup ACK,
  set SSThres=cwnd/2.
  cwnd=cwnd/2+3
  Retransmit the requested packet.
Upon every DUP ACK, cwnd=cwnd+1.
When a new ACK arrives, set cwnd=ssthres (RENO).
When an ACK arrives that ACKs all packets that were outstanding when the first drop was detected, cwnd=ssthres (NEWRENO)
RENO decreases cwnd for each pkt lost, even if pkts were lost in a busrt of losss.
NewReno decreases cwnd for each burst of losses
SN: 15MSS. L=1MSS
4000
4000
0
11000
11000
4000

## Slide 58: AIMD Performance
Q1: What is the data rate?
  How many pkts are send in a RTT?
  Rate = cwnd / RTT
cwnd
4
5
6
Seq#
(MSS)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
2
3
4
5
5
6
7
8
9
10
11
12
13
14
15
4.25
4.5
4.75
5.2
5.4
5.6
5.8
Q2: How fast does cwnd increase?
  How often does cwnd increase by 1
  Each RTT, cwnd increases by 1
dRate/dt = 1/RTT (linear in time)
RTT
RTT

## Slide 59: TCP Behavior (version 1)
drops
cwnd grows linearly (in time), and then drops by half when a loss is detected.
Thus, during AIMD, cwnd vs time looks like saw-tooth pattern
time
cwnd

## Slide 60: TCP Start up
(Suppose MSS = 1000B = 8000b)
= 100Mbps/8000b/MSS = 12500MSS/sec
Facts
cwnd grows linearly in time, with a rate of 1MSS per RTT
TCP sends a cwnd’s worth of bytes each RTT
If cwnd(0) = 1, how long until cwnd = cwnd*?
Slow Start – to speed things up
  Initially, cwnd = cwnd0 (typical 1, 2 or 3 MSS)
  When an non-dup ack arrives
    cwnd = cwnd + 1
  When a pkt loss is detected, exit slow start
What is the optimal size of cwnd over a connection with 100Mbps and RTT=100msec?
1250MSS * 100msec/MSS
 100msec/RTT = 1250 MSS/RTT = cwnd*
100Mbps
Question:
Question:
= 125sec
… kind of a long time.

## Slide 61: TCP Slow Start
cwnd
inflight
ssthresh
SN: 1MSS. L=1MSS
AN=2000
Slow Start
  Initially, cwnd = cwnd0 (typical 1, 2 or 3 MSS)
  When an non-dup ack arrives: cwnd = cwnd + 1
  When a pkt loss is detected via triple dup-ACK, enter AIMD
SN: 2MSS. L=1MSS
AN=3000
SN: 3MSS. L=1MSS
AN=4000
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
AN=5000
AN=6000
AN=7000
AN=8000
SN: 8MSS. L=1MSS
SN: 9MSS. L=1MSS
SN: 10MSS. L=1MSS
SN: 11MSS. L=1MSS
SN: 12MSS. L=1MSS
SN: 13MSS. L=1MSS
SN: 14MSS. L=1MSS
SN: 15MSS. L=1MSS
AN=8000
AN=8000
AN=8000
AN=8000
AN=8000
AN=8000
AN=8000
SN: 8MSS. L=1MSS
2000 0 0
1000 0 0
1000 1000 0
2000 1000 0
2000 2000 0
3000 1000 0
3000 2000 0
3000 3000 0
4000 3000 0
4000 2000 0
4000 4000 0
5000 4000 0
5000 5000 0
6000 5000 0
6000 6000 0
7000 6000 0
7000 7000 0
8000 7000 0
8000 8000 0
7000 8000 4000
8000 8000 4000
9000 9000 4000
10000 10000 4000
SN: 16MSS. L=1MSS
SN: 17MSS. L=1MSS
SN: 8MSS. L=1MSS
3-dup ack
Enter AIMD
11000 11000 4000
AN=16000

## Slide 62: Performance of TCP Slow Start
cwnd
inflight
ssthresh
SN: 1MSS. L=1MSS
AN=2000
SN: 2MSS. L=1MSS
AN=2000
SN: 3MSS. L=1MSS
AN=2000
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
AN=2000
AN=2000
AN=2000
AN=2000
SN: 8MSS. L=1MSS
SN: 9MSS. L=1MSS
SN: 10MSS. L=1MSS
SN: 11MSS. L=1MSS
SN: 12MSS. L=1MSS
SN: 13MSS. L=1MSS
SN: 14MSS. L=1MSS
SN: 15MSS. L=1MSS
AN=2000
AN=2000
AN=2000
AN=2000
AN=2000
AN=2000
AN=2000
SN: 8MSS. L=1MSS
1000 0 0
1000 1000 0
2000 1000 0
2000 2000 0
3000 2000 0
3000 3000 0
4000 3000 0
4000 4000 0
5000 4000 0
5000 5000 0
6000 5000 0
6000 6000 0
7000 6000 0
7000 7000 0
8000 7000 0
8000 8000 0
7000 8000 4000
8000 8000 4000
9000 9000 4000
10000 10000 4000
SN: 16MSS. L=1MSS
SN: 17MSS. L=1MSS
SN: 8MSS. L=1MSS
3-dup ack
Enter AIMD
11000 11000 4000
RTT
~RTT
~RTT
How quickly does cwnd increase during slow start?
How much does it increase in 1 RTT?
It roughly doubles each RTT – it grows exponentially
dcnwd/dt = 2 cwnd

## Slide 63: TCP Behavior (Version 2)
Slow start
Congestion avoidance
drops
drop
Initially, cwnd grows exponentially.
After a drop in slow start, TCP switches to AIMD (congestion avoidance)
In AIMD, cwnd grows linearly (in time), and then drops by half when a loss is detected (saw-tooth)

## Slide 64: Slow start
The exponential growth of cwnd during slow start can get a bit out of control.
To tame things:
Initially:
  cwnd = 1, 2 or 3
  SSThresh = SSThresh0 (e.g., 44MSS)
When an new ACK arrives
  cwnd = cwnd + 1
  if cwnd >= SSThresh, go to congestion avoidance
  If a triple dup ACK occures, cwnd=cwnd/2 and go to congestion avoidance

## Slide 65: TCP Slow Start
cwnd
inflight
ssthresh
SN: 1MSS. L=1MSS
AN=2000
Slow Start
  Initially, cwnd = cwnd0 (typical 1, 2 or 3 MSS), ssthresh=ssthresh0
  When an non-dup ack arrives: cwnd = cwnd + 1
  When a pkt loss is detected via triple dup-ACK or cwnd==ssthresh, enter AIMD
SN: 2MSS. L=1MSS
AN=3000
SN: 3MSS. L=1MSS
AN=4000
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
AN=5000
AN=7000
AN=8000
AN=9000
SN: 8MSS. L=1MSS
SN: 9MSS. L=1MSS
SN: 10MSS. L=1MSS
SN: 11MSS. L=1MSS
SN: 12MSS. L=1MSS
2000 0 4000
1000 0 4000
1000 1000 4000
2000 1000 4000
2000 2000 4000
3000 1000 4000
3000 2000 4000
3000 3000 4000
4000 3000 0
4000 4000 0
4250 4000 0
4500 4000 0
4750 4000 0
5000 4000 0
5000 5000 0
Enter AIMD
Hit SS thresh

## Slide 66: TCP Behavior (version 3)
Slow start
Congestion avoidance
drops
Cwnd=ssthresh
Slow start
Congestion avoidance
drops
drop
cwnd
cwnd

## Slide 67: cwnd During Time out
Detecting losses with time out is considered to be an indication of severe congestion
When time out occurs:
  ssthresh = cwnd/2
  cwnd = 1
  RTO = 2xRTO
  Enter slow start

## Slide 68: TCP and TimeOut
cwnd
8000
inflight
0
ssthresh
0
8000
1000
0
8000
8000
0
2000
1000
4000
SN: 1MSS. L=1MSS
SN: 2MSS. L=1MSS
SN: 3MSS. L=1MSS
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
SN: 8MSS. L=1MSS
Timeout
RTO
AN=2000
SN: 1MSS. L=1MSS
SN: 2MSS. L=1MSS
1000
1000
4000
2000
0
4000
1000
0
4000
SN: 3MSS. L=1MSS
SN: 4MSS. L=1MSS
SN: 5MSS. L=1MSS
SN: 6MSS. L=1MSS
SN: 7MSS. L=1MSS
SN: 8MSS. L=1MSS
SN: 9MSS. L=1MSS
SN: 10MSS. L=1MSS
SN: 11MSS. L=1MSS
AN=3000
AN=4000
AN=5000
AN=6000
AN=7000
AN=8000
SN: 11MSS. L=1MSS
2000
2000
4000
3000
3000
4000
4000
4000
0
Exit SS, enter AIMD
4250
4000
0
4500
4000
0
4750
4000
0
5000
4000
0
5000
5000
0
When timeout occurs:
  ssthresh = cwnd/2
  cwnd = 1
  RTO = 2xRTO
  Enter slow start

## Slide 69: RTO Doubling During Time out
RTO (e.g., 250ms)
RTO=min(2xRTO, 64s)
RTO (e.g., 500ms)
RTO=min(2xRTO, 64s)
RTO (e.g., 1000ms)
RTO=min(2xRTO, 64s)
Give up if no ACK for ~120 sec
RTO During Timeout
RTO is doubled after a timeout occurs
This doubling continues until a maximum RTO is reached (e.g., 64s)
The connection is terminated after some time limit (e.g., 120s)
When a new ACK arrives, the RTO is reset to the original value

## Slide 70: TCP Behavior
slow start
congestion avoidance (AIMD)
drops
cwnd=ssthresh
drops
drop
drops
drop
timeout
ssthresh
ssthresh
slow start
slow start
AIMD
congestion avoidance (AIMD)
slow start
congestion avoidance (AIMD)

## Slide 71: TCP Tahoe (very old version of TCP)
additive increase
drops
Every loss is like a timeout
ssthresh = cwnd/2
cwnd = 1
Enter slow start until cwnd==ssthresh, and then additive increase
slow start
slow start
slow start
additive increase
ssthresh
ssthresh
ssthresh

## Slide 72: Summary of TCP congestion control
Theme: probe the system.
  Slowly increase cwnd until there is a packet drop. That must imply that the cwnd size (or sum of windows sizes) is larger than the BWDP.
  Once a packet is dropped, then decrease the cwnd. And then continue to slowly increase.
Two phases:
  slow start (to get to the ballpark of the correct cwnd)
  Congestion avoidance, to oscillate around the correct cwnd size.
Connection
establishment
Slow-start
Congestion
avoidance
cwnd>ssthress
or Triple dup ack
timeout
Connection
termination
timeout

## Slide 73: Slow start state chart

## Slide 74: Congestion avoidance state chart

## Slide 75: TCP sender congestion control
State | Event | TCP Sender Action | Commentary
Slow Start (SS) | ACK receipt for previously unacked data | cwnd = cwnd + MSS, If (cwnd > Threshold) set state to “Congestion Avoidance” | Resulting in a doubling of cwnd every RTT
Congestion Avoidance (CA) | ACK receipt for previously unacked data | cwnd = cwnd + MSS2 / cwnd | Additive increase, resulting in increase of cwnd by 1 MSS every RTT
SS or CA | Loss event detected by triple duplicate ACK | ssthresh= cwnd/2, cwnd = ssthresh, Set state to “Congestion Avoidance” | Fast recovery, implementing multiplicative decrease. cwnd will not drop below 1 MSS.
SS or CA | Timeout | ssthresh = cwnd/2, cwnd = 1 MSS, Set state to “Slow Start” | Enter slow start
SS or CA | Duplicate ACK | Increment duplicate ACK count for segment being acked | Cwnd and ssthresh changed

## Slide 76: TCP Performance 1: ACK Clocking
What is the maximum data rate that TCP can send data?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 1 Gbps/pkt size
= 1 pkt each 12 usec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
The sending rate is the correct date rate. No congestion should occur!
This is due to ACK clocking; pkts are clocked out as fast as ACKs arrive

## Slide 77: TCP Performance 1: ACK Clocking
What is the value of cwnd that achieve the maximum data rate?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
The sending rate is the correct date rate. No congestion should occur!
This is due to ACK clocking; pkts are clocked our as fast as ACKs arrive
We want: TCP Data rate = Bottleneck data rate
From before, TCP Data rate = cwnd/RTT
Bottleneck data rate in pkts/sec = bit-rate/pkt size
Bottleneck data rate in bytes/sec = bit-rate/8
We want cwnd so that: cwnd/RTT = bit-rate/pkt size
Or, cwnd = bit-rate/pkt size * RTT
To put it another way cwnd = data rate of bottleneck link * RTT
Or cwnd = bandwidth delay product

## Slide 78: TCP Performance 1: ACK Clocking
Are there any pkts in any queue when cwnd = bandwidth delay product? No
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
We select this special cwnd so that the the send rate is exactly the bottleneck link rate

## Slide 79: TCP Performance 1: ACK Clocking
What happens as the number cwnd increases beyond BWDP?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
Let BWDP = bandwidth delay product = bottleneck link rate/pkt size * RTT
Cwnd = BWP
  Packets leave the sender at exactly the bootleneck rate
As soon as the packet is transmitted, the next packet arrives. And is transmitter

## Slide 80: TCP Performance 1: ACK Clocking
What happens as the number cwnd increases beyond BWDP?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
Let BWDP = bandwidth delay product = bottleneck link rate/pkt size * RTT
Cwnd = BWP
  Packets leave the sender at exactly the bootleneck rate
As soon as the packet is transmitted, the next packet arrives. And is transmitter
If cwnd = 2*bwdp => bwdp worth of pkts in the buffer
If buffer size is bwdp, then no drops
Now, if cwnd=2*bwdp+1, there is a drop
=> TCP will set cwnd to = bwdp
If cwnd<bwpd, the bottleneck link is not fully utilized

## Slide 81: TCP Performance 1: ACK Clocking
What happens as the number cwnd increases beyond BWDP?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
Let BWDP = bandwidth delay product = bottleneck link rate/pkt size * RTT
Cwnd = BWP
  Packets leave the sender at exactly the bootleneck rate

## Slide 82: TCP Performance 1: ACK Clocking
What happens as the number cwnd increases beyond BWDP?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
Let BWDP = bandwidth delay product = bottleneck link rate/pkt size * RTT
Cwnd = BWP
  Packets leave the sender at exactly the bootleneck rate

## Slide 83: TCP Performance 1: ACK Clocking
What happens as the number cwnd increases beyond BWDP?
10Mbps
1Gbps
1Gbps
source
destination
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 10 Mbps/pkt size
= 1 pkt each 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that ACKs are sent: ACK 1 pkts = 10 Mbps/pkt size
= 1 ACK every 1.2 msec
Rate that pkts are sent = 1 pkt for each ACK
= 1 pkt every 1.2 msec
Let BWDP = bandwidth delay product = bottleneck link rate/pkt size * RTT
After one RTT,
  cwnd = cwnd + 1
  At that time, two pkts are sent back-to-back

## Slide 84
Data rate = Bottleneck data rate
Data rate = Cwnd/rtt
Bottleneck data rate = bit-rate/pkt size
Cwnd/rtt = bit-rate/pkt size
Cwnd = rtt * bit-rate/pkt size
Cwnd = data rate of bottleneck link * RTT
Cwnd = band width (of bottleneck link) delay product

## Slide 85: TCP throughput

## Slide 86: TCP throughput

## Slide 87: TCP AIMD Throughput
w
w/2
Mean value
= (w+w/2)/2
= w 3/4
Average throughput = cwnd/RTT = w 3/4/RTT
time
cwnd
drops
What is the loss probability?
In one cycle, one pkt is lost.
How many pkts are sent in one cycle?
cycle
What is the relationship between loss probability and throughput?

## Slide 88: TCP Throughput
How many packets sent during one cycle (i.e., one tooth of the saw-tooth)?
w/2 + (w/2+1) + (w/2+2) + …. + (w/2+w/2)
w/2 +1 terms
= w/2  (w/2+1) + (0+1+2+…w/2)
= w/2  (w/2+1) + (w/2(w/2+1))/2
= (w/2)2 + w/2 + 1/2(w/2)2 + w/4
= 3/2(w/2)2 + 3/2(w/2)
 3/8 w2
One out of 3/8 w2 packets is dropped.
Loss probability of p = 1/(3/8 w2)
Combining with the first eq.
The “tooth” starts at w/2, increments by one, up to w
w
w/2
time
cwnd

## Slide 89: TCP Fairness
Fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2

## Slide 90: Why is TCP fair?
Two competing sessions:
Additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 91: RTT unfairness
Throughput = sqrt(3/2) / (RTT * sqrt(p))
A shorter RTT will get a higher throughput, even if the loss probability is the same
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2
Two connections share the same bottleneck, so they share the same critical resources
A yet the one with a shorter RTT receives higher throughput, and thus receives a higher fraction of the critical resources

## Slide 92: Fairness (more)
Fairness and UDP
Multimedia apps often do not use TCP
  do not want the rate throttled by congestion control
Instead use UDP:
  pump audio/video at constant rate, tolerate packet loss
Research area: TCP friendly
Fairness and parallel TCP connections
nothing prevents app from opening parallel connections between 2 hosts.
Web browsers do this
Example: link of rate R supporting 9 connections;
  new app opens 1 TCP, gets rate R/10
  new app opens 9 TCPs, gets R/2 !

## Slide 93: TCP problems: TCP over “long, fat pipes”
Example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
Requires window size W = 83,333 in-flight segments
Throughput in terms of loss rate:
➜ p = 2·10-10
  Random loss from bit-errors on fiber links may have a higher loss probability
New versions of TCP for high-speed long delay connections
p
RTT
MSS
×
22
.
1

## Slide 94: TCP over wireless
In the simple case, wireless links have random losses.
These random losses will result in a low throughput, even if there is little congestion.
However, link layer retransmissions can dramatically reduce the loss probability
Nonetheless, there are several problems
  Wireless connections might occasionally break.
    TCP behaves poorly in this case.
  The throughput of a wireless link may quickly vary
    TCP is not able to react quick enough to changes in the conditions of the wireless channel.

## Slide 95: Chapter 3: Summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation and implementation in the Internet
  UDP
  TCP
Next:
leaving the network “edge” (application, transport layers)
into the network “core”